## Slide 1: Product Team Update Technology Roadmap (26FE15)

## Slide 2: Technology Roadmap Process Enhancements
Restructured the Tech Roadmap
  Manage project data and progress
  Manage and assess risk
  Improve user interface to more efficiently
Incorporate Milestone Management
  Provide initiative status visibility
  Facilitate advanced planning
Improve Tech Roadmap Visibility
  Look Across/Current Engineering
  Leverage Tech Roadmap initiatives with CIP bundling opportunities
  CIP linkage and review with Application teams

## Slide 3: Technology Roadmap Process
Milestone 1
Milestone 0
Milestone 2
Milestone 3
Milestone 4
Milestone 5
Process
Proof of Concept
DEV
PV
Production
Review w/ Product Team
Risk Assessment
Big Bang Initiatives
Davis
Supporting Activities
Staff Linkage
New
Future
Zuraski
Core
Haller, Sizelove
Current / CIP
Burns, Davis
Brush CIP Workshops
Huang
Red = Date Delayed
Yellow = Date at Risk
Green = Date on Track
No longer tracked by Tech Roadmap
In a Program at SOP
Ready to Use –
On the Shelf
Ready for Project Transfer
Product Team Review & Approval
Concept
Weekly Meetings to Review Status
DV
Validation in Process
Closed
Note: Initiatives may go into Tech Roadmap if further development is required or directly to ECR/CR/CRB
CIP Advanced Planning Roadmap/Overlay
Linkage to Program Timing, Bundled Validation Windows
and Target SOP Windows
Core – CAT 1
Application
Singh

## Slide 4: Motive Ranking Visibility and Discipline

## Slide 5: Programs by Year
GEOFF’S CHART

## Slide 6: Torque Sensor

## Slide 7: FE142: LOW COST SMALL DIAMETER TORQUE SENSOR
Description
  Develop torque sensor for EPS application
Motivation
  To reduce outer diameter of torque sensor
  To reduce cost of torque sensor
  To improve gain of the linear region of operation
  To improve rotational accuracy of the sensor

## Slide 8
Lower rotor disk 2
Lower rotor
Disk 1
Upper rotor
Plastic

## Slide 9: FE142: LOW COST SMALL DIAMETER TORQUE SENSOR
Upper rotor with axially magnetized magnets
Lower rotor placed axially on one side of the upper rotor
A. Lower rotor
B. Upper rotor
or

## Slide 10
Current production IPM type torque sensor

## Slide 11: FE142: LOW COST SMALL DIAMETER TORQUE SENSOR
Results
Gain and Linearity
Higher gain achieved
Good linearity

## Slide 12: FE142: LOW COST SMALL DIAMETER TORQUE SENSOR
Results
Comparison with Prior Art Designs
Parameter | Production design | Proposed design
Total magnet volume | 1305 mm3 | Reduction by at least 20% (for sintered magnet design)
Outermost diameter | 51.88 mm | Reduction by at least 4mm
Magnet volume reduction
Outer diameter reduction
Ripple reduction
Flux density [Gauss]
Chart: 
| CP-Sintered magnet | Proposed-Sintered magnet | Proposed-Ring magnet
PP-Ripple at 4 Deg | 6.7392 | 2 | 2

## Slide 13: FE142: LOW COST SMALL DIAMETER TORQUE SENSOR
A. Lower rotor – manufacturing challenges
Introduction of notches
Disk thickness =1.5mm
Disk thickness =0.65 mm for silicon steel

## Slide 14: FE142: LOW COST SMALL DIAMETER TORQUE SENSOR
B. Upper rotor – manufacturing challenges
(Sintered magnet design)
(Ring magnet design)
High residual flux density of magnet
Magnet expensive
Low residual flux density of magnet
Less expensive magnet

## Slide 15: FE142: LOW COST SMALL DIAMETER TORQUE SENSOR
Performance with modified geometry and property- Post Adjustment
Sensor @ nominal position
Parameter | Initial Proposal-Ring Magnet | Proposed Design-Post Adjustments
Outermost diameter | 46.76 mm | 47.06 mm
Linear region gain | 27 Gauss/deg | 27.16 Gauss/deg
Max. peak-peak ripple | 2 Gauss | 2.5 Gauss
Gain:
Parameter | Production design | Proposed design
Total magnet volume | 1305 mm3 | Injection molded magnet. Cheaper than sintered.
Outermost diameter | 51.88 mm | 47.06 mm
Linear region gain | 25.25 Gauss/deg | 27.16 Gauss/deg
Max. peak-peak ripple | 6.74 Gauss | 2.5 Gauss
Comparison between initial and final proposed design
Comparison between production and final proposed design

## Slide 16: Closed Loop Steering Control (MRA Pursuit)

## Slide 17: EPS Performance and Robustness Evolution
Steering Feel Performance
Steering Feel Robustness
Early EPS
Algorithm enhancements to address variations (friction, wear, temp, etc)
Open Loop
EPS
Development focused on steering feel performance to meet/exceed hydraulic steering
Closed Loop
EPS
Technology change to address variations (friction, wear, temp, etc)
EPS
Optimized
robustness & feel
Algorithm enhancements to address special vehicle conditions (oversteer, understeer, low-mu, etc)

## Slide 18
Criteria | Open-Loop Control | Closed-Loop Control
EPS Open-Loop Control vs. Closed-Loop Control
Road Feel / Vehicle Condition Perception of mu-change, uneven surfaces, bank angle, over steer, under steer, … | Natural balance of forces reflect road surface and vehicle condition | Requires special detection and control action to reflect changes in the road surface and vehicle condition
Disturbance Rejection Capability for rejecting disturbances from road, motor, vehicle, etc. | Requires specific algorithms and tuning | Closed-loop control inherently rejects disturbances, depending on disturbance frequency and servo bandwidth
Performance Robustness Robustness to variations in manufacturing, friction, wear, usage, ... | Dedicated algorithms required to manage performance variation (Friction Learn/Comp Temperature Comp, SRS Comp, Active Pull Comp) | Compensates for variations by design to give consistent performance
Tuning Interface Relationship between tuning parameters and steering feel | Friction & Damping: compensate effects to get desired friction & damping feel Assist: Indirect relationship to driver torque. Effort: open-loop estimation of driver torque | Friction & Damping: directly calibrate desired steering feel performance Effort: direct relationship to driver torque
Tuning Process Coupling among the tuning parameters, tuning difficulty and time | Desired feel is achievable but requires a structured tuning process and iterations (processes are well developed) | High level functions such as effort, return, and damping have less coupling
Tuning Portability Ease of porting tuning across platforms | Limited portability, but mature industry experience | Tuning calibrations potentially portable, but depends on vehicle response Some calibrations require vehicle test data

## Slide 19: EPS Closed-Loop Control Technology – Status and Timeline
Concept generation
Literature survey
Market analysis
2012
Control design
Numerical simulation
Control strategy selection
AUTOSAR Autocoding
Prototype software build
Controller and gear build
Bench test
Vehicle integration
Internal vehicle build
Demonstrated performance to GM
Advanced feature development
Operating space transition
Continuous improvement
Present
Winter test
Closed loop control strategy finalization
Prepare for commercial offering
Safety concept
Future

## Slide 20: Closed-Loop Control System Architecture
Target Generator
Tracking
Control
Steering System
Vehicle
Sensors/
Observers
Desired
HwTrq
Compensation
Motor
Control
+
Bandwidth
Stability
Steering State
Rack Force
Vehicle State
Surface
Friction
Inertia
Road Wheel Imbalance
Vehicle Lead/Pull
Effort
Damping
Hysteresis
Return

## Slide 21: Closed Loop Steering Control

## Slide 22: MRA Function Implementation Status

## Slide 23
MRA Closed Loop Sub-functions

## Slide 24: High Ratio CEPS

## Slide 25: Higher Ratio (31:1) A/M

## Slide 26: Status
31:1 First build complete
  CMM data good after 2 iterations of gear cutting for over-ball adjustments
  Assembly run in at 60 Nm
  Backdrive friction set to ~1.2 N-m average
    Once per rev similar to Haitec production (see following slides)
  Contact pattern looks good visually – measurement data pending (see following slides)
  Marginal Efficiency average measured ~87.5% (see following slides)
  First running noise test set for Monday 2Mr15
28:1 and 30:1 first cut gears are being inspected on CMM
  Adjustments may be required
31:1 First build complete
  CMM data good after 2 iterations of gear cutting for over-ball adjustments
  Assembly run in at 60 Nm
  Backdrive friction set to ~1.2 N-m average
    Once per rev similar to Haitec production (see following slides)
  Contact pattern looks good visually – measurement data pending (see following slides)
  Marginal Efficiency average measured ~87.5% (see following slides)
  First running noise test set for Monday 02MR15 28:1 and 30:1 first cut gears are being inspected on CMM
  Adjustments may be required

## Slide 27: 31:1 Backdrive Friction Data

## Slide 28: 31:1 Contact Pattern Pictures

## Slide 29: 31:1 Efficiency Data
New 31:1
REF Production Gamma 22:1

## Slide 30: Motor Optimization

## Slide 31: PP-124: Cost Optimized Motor Design (IPM/skew/pole shape/WIH)
Description
  Develop Cost Optimized Motor
Motivation (10)
  Reduce Material cost in Motor
Deliverables
  Determine if Larger OD Rotor is a Cost Advantage
  Determine if Higher Grade Magnets vs cost is a feasible option
  Determine which stator / winding design is optimal for cost
  Determine if shape of magnet has cost impact
Timing
  Fiasa & PSA BMPV (2016 - SOP)
Team Members/Customers
  Rakib Islam
  Bryan Williams
  Ken Webber
  Steve Collier-Hallman
  John Redwine

## Slide 32: Cost Motor Model and Cogging Cancellation
Note: Needle, SPM 2 Step R1=R2 Assumes 0.25 Volt Cancellation
Cogging Torque

## Slide 33: PP-126: Heat Management for Motor
Description
  Reduce Motor generated heat from Segment/Needle Stator designs
Motivation (9)
  Segment and Needle Wind Motors with plastic Insulators generate more heat than Shed Wound motors
Deliverables
  Determine if gap filler can be added prior to winding to get direct heat transfer to stator
  Determine if thermally conductive coatings (Bergquist epoxy coat) on stator instead of plastic insulator reduces motor thermals.
  Determine which stator / winding design is optimal for thermals
Timing
  Fiasa & PSA BMPV (SOP - 2016)
Team Members/Customers
  Rakib Islam
  Bryan Williams
  Ken Webber
  Joanne Tersigni
  Julie Kleinau